## Slide 1: UGPOST Kinematics
Stan Suderman

## Slide 2: Kinematic Variables
Kinematic variables define machine tool specific information used by the event generator.
Kinematic variables defined by the event handler, determine how the event generator converts the x,y,z,i,j,k toolpath coordinates into machine tool coordinates.
Kinematic variables are also used to define the basic type of machine: lathe, mill or wedm.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3: Basic Types of Machines
mom_kin_machine_type
  lathe
  3_axis_mill
  4_axis_head
  4_axis_table
  5_axis_dual_table
  5_axis_dual_head
  5_axis_head_table
  2_axis_wedm
  4_axis_wedm
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Lathe
When the machine type is set to lathe, all coordinates in the tool path will be mapped to lathe coordinates.
UG Tool Path
Machine Blocks
x,y,z --> x,0,z
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: Mill
When the machine type is set to a mill type, the event generator will map the x,y,z,i,j,k toolpath coordinates to x, y, z, 4th axis rotary & 5th axis rotary coordinates.
UG Tool Path
Machine Blocks
x,y,z,i,j,k --> x,y,z,a,b
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: Mill
The machine tool type defines the number of axes.
Each rotary axis has the following:
  a plane of rotation
  travel limits
  direction of rotation
  zero position.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Circles
mom_kin_arc_output_mode
  This kinematic variable determines the data and number of blocks that will be generated for arcs in the toolpath.
FULL_CIRCLE
  A circle_move event will be generated in 360 degree increments.
QUADRANT
  A circle_move event will be generated for each quadrant boundary crossed
LINEAR
  This setting will cause the event generator to break the arcs into linear goto events.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Circles
mom_kin_arc_valid_plane
  This kinematic variable determines the planes that the event generator will generate circle_move events.
XYZ
  Arcs will be generated in all three principal planes.
XY
  Arcs will generated only in the XY plane.
YZ
  Arcs will generated only in the YZ plane.
ZX
  Arcs will generated only in the ZX plane.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: Exercise 1
Specify the kinematics variables to make a five axis machine with the following features.
  4th axis -- Tilting A in YZ plane, limits are +/- 20 degrees.
  5th axis -- Swiveling head C in XY plane, limits are 0-360.
  The pivot point is 10 inches.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Exercise 2
Specify the kinematics variables to output arcs at every quadrant boundary and only in the XY plane.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: Solution 1
set mom_kin_machine_type 5_axis_dual_head
set mom_kin_4th_axis_plane YZ
set mom_kin_4th_axis_min_limit -20
set mom_kin_4th_axis_max_limit 20
set mom_kin_5th_axis_plane XY
set mom_kin_5th_axis_min_limit 0
set mom_kin_5th_axis_max_limit 360
set mom_kin_pivot_gauge_offset 10
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: Solution 2
set mom_kin_output_mode quadrant
set mom_kin_valid_plane xy
Notes: <number>
<footer>
<header>
<date/time>