## Slide 1: Definition File for UGPOST
Stan Suderman

## Slide 2: Definition File
The definition file defines the format and content of the blocks that can be output by UG Post
  Structure
  Format
  Address
  Block Template
  Include

## Slide 3: MACHINE name
INCLUDE {name_1, name_2, ...}
FORMATING {
WORD_SEPARATOR “ string“
END_OF_LINE “ string“
...
ADDRESS name
{ ... }
BLOCK_TEMPLATE name {}
}

## Slide 4: Source from different machines
INCLUDE {name_1, name_2, ..., name_n}
name_1 = name of an existing definition file
The system will source this file into the loaded file.

## Slide 5: Definition File Elements
WORD_SEPARATOR “string“
  string between each address
END_OF_LINE “string“
  string at the end of each line
SEQUENCE name start increment frequency
  name = block template for line number
  start = start value
  increment frequency = increment value
  frequency = every value
  SEQUENCE NUMBER 1 1 1

## Slide 6: Format
FORMAT name &abcdef
  a = + or _ “+” means output the plus sign, “_” means suppress the plus sign.
  b = 0 or _ “0” means output leading zeros, “_” means suppress leading zeros.
  c = {0,1,…,9} Maximum number of digits to left of decimal.
  d = . or _ “.” means output the decimal, “_” means don’t output the decimal
  e = {0,1,…,9} Maximum number of digits to right of decimal.
  f = 0 or _ , “0” means output trailing zeros, “_” means suppress trailing zeros.

## Slide 7: Format
FORMAT Coordinate “&__3.4_”
This format will output a number with no plus sign, no leading or trailing zeros, 3 digits to left of the decimal and 4 to right with a decimal point.
Example: X12.34

## Slide 8: Format
FORMAT name C_Format_String
  s = string (“hello”)
  d = integer (“5”)
  f = floating double (“3.14...”)
  g = exponent double (“1e2”)
  %0i,jf 0=leading 0
  i=total length of number
  j=precision

## Slide 9: Zero Format
ADDRESS X {
ZERO_FORMAT zero_coord
FORMAT Coordinate
MAX 9999.9999
MIN -9999.9999
FORCE off
}
This option allows users to control how zero is output. Zero_format only controls the output when the value to be output is exactly zero.
  FORMAT zero_coord “0_01.0_”

## Slide 10: Sequence
SEQUENCE seqn 1 1 3
N001
..
..
N002
SEQUENCE seqn 1 1 1
N001
N002
N003

## Slide 11: Address
ADDRESS X {
FORMAT name
FORCE <Always | Once | Off>
MAX number <Abort | Warning | Truncate>
MIN number <Abort | Warning | Truncate>
ZERO_FORMAT coordinate
LEADER string
TRAILER string
}

## Slide 12: Address
ADDRESS motion_g {
FORMAT Socket
FORCE Never
MIN 0 Abort
MAX 99 Abort
LEADER “G“
TRAILER “ “
}

## Slide 13: BLOCK_TEMPLATE
BLOCK_TEMPLATE name {
Address_Name [Address_Expression]
\nows \opt \ldr=string1
\trl1 =string2
}

## Slide 14: BLOCK_TEMPLATE
BLOCK_TEMPLATE cycle_drill {
motion_g [$mom_sys_cycle_drill_code]
X [$mom_cycle_fedto_pos(0)]
Y [$mom_cycle_fedto_pos(1)]
Z [$mom_ cycle_fedto_pos(2)]
R [$mom_ cycle_rapto_pos(2)]
F [$mom_feed_rate]
}

## Slide 15: Exercise 1
- NC-code with space between the addresses
- NC-code without space between the addresses

## Slide 16: Exercise 2
- Sequence number (10,20,30)
Start at 10 and increment by 10
  N10 G1 X10
  N20 Y20
  N30 Y40
- Sequence number (5,..,15,...25)
Start at 5, increment by 10, and output every other block
  N5 G1 X10
  Y20
  N15 Y40

## Slide 17: Exercise 3
- Sequence number format (10,20,30,40)
No leading zeroes
- Sequence number format (0010,0020,0030,0040)
Output leading zeroes
- Coordinates with 5 whole digits, 3 fractional digits, no leading zeros, trailing zeros and no decimal point.
- Coordinates with 4 whole digits, 4 fractional digits, leading and trailing zeros with no decimal point.

## Slide 18: Exercise 4
- G1 Y... X.... Z.…
  Reverse x and y words for linear moves.
- G1 Z... X.... Y.…
  Output z first for linear moves.

## Slide 19: Exercise 5
- instead of “G1” “Gll”
- instead of “G0” for rapid xy move “rapid”

## Slide 20: Exercise 6
- instead of “X” “X-Coord.”
- when F is greater than 10, then the system should stop and output an error message.

## Slide 21: Exercise 7
- Make the X word come out on all motion blocks.

## Slide 22: Exercise 8
-Make the I,J,K output circle center coordinates on arc motion blocks.

## Slide 23: Solution 1
- WORD_SEPARATOR “ “
- WORD_SEPARATOR ““

## Slide 24: Solution 2
- SEQUENCE seqn 10 10 1
- SEQUENCE seqn 5 10 3

## Slide 25: Solution 3
- FORMAT Naddress “&__4___”
- FORMAT Naddress “&__40__”
ADDRESS N {
FORMAT Naddress
FORCE off
}
- FORMAT Coordinate “&__5_30”
- FORMAT Coordinate “&+04_40”

## Slide 26: Solution 4
BLOCK_TEMPLATE linear {
G[$mom_sys_linear_code]
Y [$mom_pos(1)]
X [$mom_pos(0)] Z [$mom_pos(2)]
}
BLOCK_TEMPLATE linear {
G [$mom_sys_linear_code]
Z [$mom_pos(2)]
X [$mom_pos(0)] Y [$mom_pos(1)]
}

## Slide 27: Solution 5
BLOCK_TEMPLATE linear {
G[11]
X [$mom_pos(0)] Y [$mom_pos(1)]
Z [$mom_pos(2)]
}
OR
set mom_sys_linear_code 11
BLOCK_TEMPLATE rapid_xy {
“rapid”
X [$mom_pos(0)] Y [$mom_pos(1)]
Z [$mom_pos(2)]
}

## Slide 28: Solution 6
ADDRESS X {
FORMAT Coordinate
FORCE Off
LEADER “X-Coord.”
}
ADDRESS F {
FORMAT Coordinate
FORCE Off
MAX 10 Abort
}

## Slide 29: Solution 7
ADDRESS X {
FORMAT Coordinate
FORCE Always
}

## Slide 30: Solution 8
BLOCK_TEMPLATE circle { motion_g [$mom_sys_circle_code($mom_arc_direction)]
X[$mom_pos(0)]
Y[$mom_pos(1)]
Z[$mom_pos(2)]
I[$mom_pos_arc_center(0)]
J[$mom_pos_arc_center(1)]
K[$mom_pos_arc_center(2)]
F[$mom_feed_rate]
}