## Slide 1: Post Builder
Stan Suderman

## Slide 2: Post Builder
Post Builder allows you to create and edit postprocessors.
Post Builder will read and write the following three files.
  Post.pui -- This file is the master post builder file. It contains the information that does not get written into the .tcl and .def files. It must be located in the same directory as the .tcl and .def files. DO NOT DELETE!
  Post.def -- UG Post definition file.
  Post.tcl -- UG Post event handler file.

## Slide 3: Post Builder Features
Definition of all output blocks.
Formats for all the addresses
Control of the sequence of output for:
  Start of Program
  Start of Operation
  End of Operation
  End of Program
  Tool Changes
  Canned cycles

## Slide 4: Post Builder Features
Provides a graphical, easy to use interface to create a post processor
Post Builder allows you to create Formats, Addresses, Blocks and Sequences
Provides a starting set of files for a custom post processor

## Slide 5: Exercise 1
Cd to /resource/postprocessor
Run Post Builder (type pb)
Create a new post
Save your post to the /resource/postprocessor directory.
Edit the template_post.dat file to include your new post.
Reload your configuration file or restart UG and observe your new post in the list.

## Slide 6: Exercise 2
Create a start of program sequence with the following information.
  Rewind Stop Code (#)
  G70G90G40G17G00
Save your post and run it against mypart.prt and verify your output.

## Slide 7: Exercise 3
Create a tool change block as follows.
  G91G28Z0
  M06 T0001
  T0002 (next tool number)
Save your post and run it against mypart.prt and verify your output.

## Slide 8: Exercise 4
Change the G code for Cycle/Drill to G71
Change the G code for Rapid Motion to G01 and add an R to each Rapid motion block.
Save your post and run it against mypart.prt and verify your output.

## Slide 9: Exercise 5
Change the sequence of output so that the T code always comes out after the M06 code in a tool change.
Save your post and run it against mypart.prt and verify your output.

## Slide 10: Exercise 6
Change the format of all coordinates to look like the following:
  The X position of 1.23 would be output as X12300
Save your post and run it against mypart.prt and verify your output.

## Slide 11: Exercise 7
Change the canned cycles for your post to output a block before each cycle to rapid in x and y.
  G00 X Y
  G81 X Y R Z
Save your post and run it against mypart.prt and verify your output.

## Slide 12: Exercise 8
For each of the following functions, instead of a G code, output the following text.
  G00 MOVE
  G01 L
  G02 CLW
  G03 CCW
  G81 CYC_DRL
  G83 CYC_BRK
Save your post and run it against mypart.prt and verify your output.