## Slide 1: UGPOST User Defined Event File
Stan Suderman

## Slide 2: User Defined Events (UDE)
UDEs describe the format of all APT style post commands
All UDEs are defined in a file called ude.cdl in the $UGII_BASE_DIR/mach/resource/user_def_event/ude.cdl
UDEs can be specified at the start or end of path or attached to any object in CAM (program, tool, machine tool, etc.) using the Machine Control Dialog
UDEs generate events in UG Post with all event data being passed to the post processor as mom variables.

## Slide 3: User Defined Events
EVENT spindle {
UI_LABEL "Spindle On"
CATEGORY MILL DRILL LATHE
PARAM command_status
{
TYPE o
DEFVAL "Active"
OPTIONS "Active","Inactive","User Defined"
UI_LABEL "Status” ...
The ude.cdl file defines events
A corresponding procedure in the .tcl file is required for output
Can be included in the .def file
The ude.cdl is referenced by the configuration file

## Slide 4: User Defined Events Syntax
EVENT <name>
{
POST_EVENT <post_name>
UI_LABEL <ui_name>
CLASS Type, subtype, subtype; Type, subtype, subtype;
CATEGORY Mill | Drill | Lathe | WEDM
PARAM <param_name1>
{
TYPE i | d | s | o | p DEFVAL <default value as string>
TOGGLE Off | On
OPTIONS <string1, string2, string3.......>
UI_LABEL <ui_name>
}
PARAM <param_name2>
PARAM <param_name3>
}

## Slide 5: User Defined Events
EVENT <name> defines the event "name"
POST_EVENT <post_name> specifies that the event "name" will be output to the Post Processor as an event called "post_name". This attribute of the EVENT is optional and if not specified, the event will be output to the Post Processor as an Event called "name".
UI_LABEL <ui_name> specifies that "ui_name" is a string used for the title of the dialog. This attribute of the EVENT is optional and if not specified the event name itself is used as the "ui_name".
CLASS attribute specifies the Operation sub types in which the EVENT is valid. The Type and subtype get the same meaning as in the context of Templates. This is an optional attribute and when not specified implies that the EVENT is valid for all Types and subtypes.
CATEGORY attribute specifies the Machining type (mill, lathe, wedm, .etc.) in which the Event is relevant. This attribute is optional. The Event can be specified to be relevant in more than one Machining Mode. When this attribute is not specified the Event becomes relevant in all Machining Modes.

## Slide 6: User Defined Events
PARAM <param_name1> specifies a parameter of the Event. The parameter has a name "param_name1".
  TYPE is an attribute of the PARAM and specifies the parameter type. The possible values for TYPE are:
    i - an integer
    d - a real number
    s - a string
    o - one of a possible set of options
    p - a point
  DEFVAL <default value as a string> specifies the default value of the parameter. This is an optional attribute and if not specified the following will be the defaults according to the TYPE of the parameter:
    i - default value is 0
    d - default value is 0.0
    s - default value is an empty string
    o - default value is the first one of the list of options provided
    p - default value does not apply

## Slide 7: User Defined Events
TOGGLE is an attribute of the parameter which specifies a default value and that the default value is either On or Off. The TOGGLE attribute is optional and if not specified the parameter is mandatory.
OPTIONS is a required attribute of the parameter when the TYPE is 'o'. This provides all the possible values that the parameter can have. The values are specified as comma separated strings.
UI_LABEL <ui_name> specifies that "ui_name" will be the text displayed in the dialog presented. This is an optional attribute and if not specified the "param_name1" itself is used as the "ui_name".

## Slide 8: UDE Used In Other Places
Add post commands (events) to a Program, Tool, Operation, .etc.
Add to customized dialog

## Slide 9: Exercise 1
Change the default for coolant to mist

## Slide 10: Exercise 2
Make a new user defined event with the following format:
  Load new Co-ordinate system (G54…G59)
Make an event handler for it and output the following
  G59

## Slide 11: Exercise 3
Make a new user defined event with the following format:
  Load Fixture Offset Register
Make an event handler for it and output the following
  E12

## Slide 12: Solution 1
EVENT coolant
{
POST_EVENT "coolant_on"
UI_LABEL "Coolant On"
PARAM command_status
{
TYPE o
DEFVAL "Active"
OPTIONS "Active","Inactive","User Defined"
UI_LABEL "Status"
}
PARAM coolant_mode
{
TYPE o
DEFVAL "Flood“ << “Mist”
OPTIONS "On","Flood","Mist","Tap"
UI_LABEL "Type"

## Slide 13: Solution 2 UDE
EVENT sys_offset
{
POST_EVENT "csys_load"
UI_LABEL "Co-ordinate Sys Offset"
CATEGORY Mill Drill
PARAM command_status
{
TYPE o
DEFVAL "Inactive"
OPTIONS "Active","Inactive"
UI_LABEL "Status"
}
PARAM csys_register
{
TYPE o
DEFVAL "54“
OPTIONS “54”,”55”,”56”,”57”,”58”,”59”
UI_LABEL "Co-ordinate System"
}
}

## Slide 14: Solution 2 Event Handler
In the tcl file add the following in MOM_initial_move:
MOM_do_template path_start
In the def file add the following:
BLOCK_TEMPLATE path_start {
G[00] G[90] G[$mom_csys_register]
}

## Slide 15: Solution 3 UDE
EVENT fixt_load_offset
{
POST_EVENT “fixt_load"
UI_LABEL “Load Fixture Offset"
CATEGORY Mill Drill
PARAM command_status
{
TYPE o
DEFVAL "Inactive"
OPTIONS "Active","Inactive"
UI_LABEL "Status"
}
PARAM fixt_register
{
TYPE i
DEFVAL “22“
TOGGLE Off
UI_LABEL “Fixture Offset Register"
}
}

## Slide 16: Solution 3 Event Handler
FORMAT e_code "&__2_0_"
ADDRESS E {
FORMAT e_code
MAX 99
MIN 0
FORCE off
}
BLOCK_TEMPLATE rapid_xy {
g_motion[$mom_sys_rapid_code]
X[$mom_pos(0)]
Y[$mom_pos(1)]
E[$mom_fixt_register]\opt
}