## Slide 1: UGPOST Event Handler File
Stan Suderman

## Slide 2: UG Post Architecture
UG Data Storage
UG Post
Event
Generator
Event Handler
Definition File
Output File
Event Name
variable
variable
variable
User Defined
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3: Event Generator Example
Linear Motion
  GOTO/ x, y, z, i, j, k
Event generator creates an a linear_move event with following variables.
  mom_pos -- machine tool x,y,z,a,b
  mom_prev_pos -- previous machine tool x,y,z,a,b
  mom_goto_pos -- goto in mcs
  mom_goto_tool_axis -- goto tool axis in mcs
  mom_prev_goto_pos -- previous mcs goto
  mom_prev_goto_tool_axis -- previous tool axis goto
  mom_feed_rate_per_min -- feedrate in inches/mm per minute
  mom_feed_rate_per_rev -- feedrate in inches/mm per revs
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Examples of typical events and variables loaded by the Event Generator
MOM_linear_move
  When Triggered: For each linear motion in the tool path.
  Variables Loaded:
    mom_pos(0)
    mom_pos(1)
    mom_pos(2)
MOM_circular_move
  When Triggered: For each circular motion in the tool path.
  Variables Loaded:
    mom_pos(0) mom_arc_center(0)
    mom_pos(1) mom_arc_center(1)
    mom_pos(2) mom_arc_center(2)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: MOM_do_template
MOM_do_template template_name
Generate output based upon the Block Template template_name.
Example:
MOM_do_template linear
G1 X10 Y20 Z5
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: UG Post Base File
UG Post base file contains basic procedures common to all postprocessors. This file must be sourced in every event handler.
The event generator will provide common G and M codes for many events.
M00 Stop, M01 Opstop, M02 End, M03 Spindle CLW, etc.
G00 Rapid, G01 Linear, G02 Circle CLW, etc.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: UG Post Base File
The base file contains the default processing for all events. This includes PPRINT, INSERT and other basic functions.
The base file also includes the procedure for outputting commentary information (eyewash).
The base file is supplied by UG. Any procedure in the base file may be overwritten by the user, if desired.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Event Procedure Example
proc MOM_linear_move {} {
MOM_do_template linear
}
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: MOM_output_literal
MOM_output_literal “string”
  Output a list of literals and variables as a single line.
Example:
MOM_output_literal “Operation name: $mom_path_name”
Operation name: P1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Event Procedure Example
proc MOM_start_of_path {} {
global mom_operation_type
global mom_path_name
MOM_output_literal “Operation_type: $mom_operation_type”
MOM_output_literal “Operation_name: $mom_path_name”
}
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: MOM_suppress
MOM_suppress <Always|Once|Off> address_1,...,address_n
This command will suppress the output of the address in any block template.
Always: force always
Once: force once
Off: force off
Example:
MOM_suppress Once N
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: Event Procedure Example
proc MOM_start_of_program {} {
MOM_suppress Once N
MOM_output_literal “%”
}
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Event Procedure Example
proc MOM_linear_move {} {
MOM_do_template linear
}
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: MOM_force
MOM_force <Always|Once|Off> address_1,...,address_n
The next time a block template that contains any of the addresses, the system will output the value of the address.
Always: force always
Once: force once
Off: force off
Example:
MOM_force Once X Y Z
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: Event Procedure Example
proc MOM_initial_move {} {
MOM_force Once X Y Z
MOM_do_template initial_move
...
}
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: MOM_set_seq_on
MOM_set_seq_on
Allow output of the sequence number if SEQUENCE specifier was given in the definition file.
Example:
MOM_set_seq_on
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17: MOM_set_seq_off
MOM_set_seq_off
Do not output a sequence number.
Example:
MOM_set_seq_off
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18: Exercise 1
Modify the procedure start_of_program in my_post.tcl:
  Setup a line without N but with %4711
  Setup a Header with no N
    output:
      mom_date
      mom_logname
      mom_part_name
  Setup a line to output “G40 G80 G17”
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: Exercise 2
Modify the procedure start_of_path in my_post.tcl:
  output:
    mom_operation_type
    mom_path_name
    mom_tool_name
    mom_tool_type
    mom_tool_number
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20: Exercise 3
Modify the output for the event cycle_drill
  G101 X Y E R
    X Y start position of the drill cycle
    E depth of hole
    R rapid position
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: Exercise 4
Implement in the rapid move procedure
  Instead of G0 output G1 with R
  G1 X Y Z R
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22: Exercise 5
Implement in the rapid move procedure
  For all rapid moves output F0
  G0 X Y Z F0
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: Solution 1
MOM_output_literal "(######## TASK : $mom_part_name ############)"
MOM_output_literal "(# Created By : $mom_logname)”
MOM_output_literal "(# Creation Date: $mom_date)"
MOM_output_literal "(############################################)"
MOM_suppress always N
MOM_output_literal "%4711"
MOM_suppress off N
MOM_output_literal "G70 G90"
MOM_output_literal ”G80 G40 G17"
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: Solution 2
MOM_output_literal "(----------------------------------------------------)"
MOM_output_literal "(Operation Name: $mom_path_name)"
MOM_output_literal "(Operation Type: $mom_operation_type)”
MOM_output_literal "(Tool Name: $mom_tool_name)”
MOM_output_literal "(Tool Type: $mom_tool_type)"
MOM_output_literal "(Tool Number: $mom_tool_number)"
MOM_output_literal "(----------------------------------------------------)"
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25: Solution 3
BLOCK_TEMPLATE cycle_drill {
motion_g[$mom_sys_cycle_drill_code]
X[$mom_cycle_feed_to_pos(0)]
Y[$mom_cycle_feed_to_pos(1)]
E[$mom_cycle_feed_to_pos(2)]
R[$mom_cycle_rapid_to_pos(2)]
F[$mom_feed_rate]
}
set mom_sys_cycle_drill_code 111
# create address E
ADDRESS E {
FORMAT Coordinate
MAX 9999.9999
MIN -9999.9999
FORCE off
}
Notes: <number>
<footer>
<header>
<date/time>

## Slide 26: Solution 4
set mom_sys_rapid_code 1
BLOCK_TEMPLATE rapid_xy {
motion_g[$mom_sys_rapid_code]
G[$mom_sys_output_code($mom_output_mode)]\opt
X[$mom_pos(0)]
Y[$mom_pos(1)]
“R”
}
BLOCK_TEMPLATE rapid_z {
motion_g[$mom_sys_rapid_code]
Z[$mom_pos(2)]
H[$mom_tool_adjust_register]\opt
“R”
}
Notes: <number>
<footer>
<header>
<date/time>

## Slide 27: Solution 5
set mom_sys_rapid_code 0
BLOCK_TEMPLATE rapid_xy {
motion_g[$mom_sys_rapid_code]
G[$mom_sys_output_code($mom_output_mode)]\opt
X[$mom_pos(0)]
Y[$mom_pos(1)]
“F0”
}
BLOCK_TEMPLATE rapid_z {
motion_g[$mom_sys_rapid_code]
Z[$mom_pos(2)]
H[$mom_tool_adjust_register]\opt
“F0”
}
Notes: <number>
<footer>
<header>
<date/time>