## Slide 1: UGPOST 5-Axis Kinematics
Stan Suderman

## Slide 2: Five Axis Machine Tools
The kinematics variable mom_kin_machine_type defines the machine type. For a 5 axis machine, one of the following values should be assigned to this variable based on the machine type:
5_axis_dual_table
5_axis_head_table
5_axis_dual_head

## Slide 3: Coordinate System

## Slide 4: Rotary Axes Designations
Independent axis is the rotary axis that DOES NOT change its orientation or plane of rotation when the other rotary axis moves. However, in a HEAD-TABLE type of 5-axis machine (fig-5 & 7) , the swivel head is always the independent axis (or 4th axis).
The C axis should not be set as the 4th axis.
Dependent axis (or 5th axis) is the rotary axis that DOES change its orientation or plane of rotation when the other rotary axis moves.

## Slide 5: Figure 5, Head Table

## Slide 6: Figure 7, Deckel Maho, DMC80U

## Slide 7: 4th Axis Center Offsets
The array mom_kin_4th_axis_center_offset contains the offset values of the machine tool's zero position to the center of the 4 axis table.
For the post to correctly map the part coordinate system (MCS) to the Machine Tool Coordinate System, this offset value must be correct.
The value is the distance of the machine tool's zero position to the center of the fourth axis.
mom_kin_4th_axis_center_offset(0) X distance mom_kin_4th_axis_center_offset(1) Y distance mom_kin_4th_axis_center_offset(2) Z distance

## Slide 8: 5th Axis Center Offsets
The array mom_kin_5th_axis_center_offset (the distance from the center of the fifth axis to the center of the fourth axis), contains the offset values and is used to indicate the 5th axis of rotation does not intersect the 4th axis of rotation.
To derive this vector, both axis should be at zero degrees. The value may involves two coordinates but normally one.
This perpendicular vector is measured in the plane of the 4th axis from the axis of rotation of the 5th axis to the axis of rotation of the 4th axis.
  mom_kin_5th_axis_center_offset(0) X distance mom_kin_5th_axis_center_offset(1) Y distance mom_kin_5th_axis_center_offset(2) Z distance

## Slide 9: Axis Rotation (Standard or Reverse)
This parameter controls how UGPost will translate the i,j,k tool axis information into rotary positions.
Most NC machines are Standard, rotation or swiveling is clockwise to a larger angle.
  (When in doubt use the Standard convention unless the data is incorrect for your machine tool)
The following guidelines can be used.
  In the XY plane looking down the Z axis from positive to negative, rotation clockwise to a larger angle is Standard.
  In the ZX plane looking down the Y axis from positive to negative, rotation clockwise to a larger angle is Standard.
  In the YZ plane looking down the X axis from negative to position, rotation clockwise to a larger angle is Standard.

## Slide 10: Axis Rotation (Standard or Reverse)
This parameter for each of the rotary axis is set by mom_kin_4th_axis_rotation and mom_kin_5th_axis_rotation
This variable may be set to standard or reverse as below:
  set mom_kin_4th_axis_rotation standard
  set mom_kin_5th_axis_rotation reverse
Each of the above kinematic variable may be set to standard or reverse as required by the control
For Example:
  A dual head machine, as show in figure 1, can orient the tool along a (1,0,0) vector by rotating the A axis by 90 degrees and then B axis by 90 degrees. However, if the axis rotation of the A axis is set to reverse, then the A axis angle will be -90 degrees for the same tool axis vector

## Slide 11: Figure 1, Dual Head

## Slide 12: Zero Position Offset
When both the rotary angles on a machine are set to zero, the tool should be aligned to the Z axis of the Machine Tool Coordinate System.
The zero position of a rotary axis on some machine tools, (typically dual head and head table machines) is set at a finite angular value.
This value may be defined in the kinematic variable mom_kin_4th_axis_zero_position and mom_kin_5th_axis_zero_position for the 4th and 5th axis respectively.

## Slide 13: Zero Position Offset (Example)
Refer to figure 5, head table 5 axis machine. The zero position on this machine for the head may be set to -90 degrees. When the head is at 0 degrees, the tool will be aligned with the Y axis of the Machine Tool Coordinate System, towards the table. The kinematic variables may be set in the tcl file as below : set mom_kin_4th_axis_zero_position -90.0 set mom_kin_5th_axis_zero_postion 0.0
Hence for a (0,0,1) tool axis vector will output a A rotary value of 90.0, since the zero position is at -90 degrees.

## Slide 14: Figure 5, Head Table

## Slide 15: Pivot Point
Pivot point is defined as the point about which the rotary head tilts. On a dual head machine this point is defined as the 4th axis head and 5th axis head. Many times the pivot points are co-incidental.
For Standard 5 axis head table machine or for dual head machine this point may defined by the kinematic variable : mom_kin_pivot_gauge_offset.
This offset is measured from the spindle gauge point to the point of rotation of the head.
For the Deckel Maho machine shown in figure 7, the pivot point is defined by the kinematic array variable mom_kin_gauge_to_pivot. On these machines, the pivot point lies on the 4th axis rotation vector.

## Slide 16: Figure 7, Deckel Maho, DMC80U

## Slide 17: Figure 1, Dual Head

## Slide 18: Figure 2, Dual Head Offsets

## Slide 19: Dual Head Kinematics
The following lines define the machine tool as shown in figure 1
  set mom_kin_machine_type 5_axis_dual_head set mom_kin_4th_axis_plane ZX
  set mom_kin_4th_axis_center_offset(0) 0.0 set mom_kin_4th_axis_center_offset(1) 0.0 set mom_kin_4th_axis_center_offset(2) 0.0 set mom_kin_4th_axis_rotation standard set mom_kin_4th_axis_zero_position 0.0
  set mom_kin_pivot_gauge_offset 100.00 set mom_kin_5th_axis_plane YZ set mom_kin_5th_axis_center_offset(0) XX (5th axis x-offset) set mom_kin_5th_axis_center_offset(1) YY (5th axis y-offset) set mom_kin_5th_axis_center_offset(2) ZZ (5th axis z-offset) set mom_kin_5th_axis_rotation standard set mom_kin_5th_axis_zero_position 0.0
The distance from the Machine Tool Zero to the center of the 4th axis is not needed in this type of machine and must be set to zero.

## Slide 20: Dual Table Kinematics
In the figure 3, the B table is mounted on the A table. Therefore the MCS in UG should be set to the center 5th axis table while creating operations.
If the Machine Tool Zero is not at the center of this table (Independent or 5th axis), then the distance from the Machine Tool Zero to the table center must be entered in the 4th axis center offsets kinematics variable
And the distance from 4th axis to 5th axis must be set in 5th axis center offsets kinematics variable.

## Slide 21: Figure 3, Dual Table

## Slide 22: Figure 4, Dual Table Offsets

## Slide 23: Dual Table Kinematics
The following lines define the machine tool as shown in figure 3
  set mom_kin_machine_type 5_axis_dual_table set mom_kin_4th_axis_plane YZ set mom_kin_4th_axis_center_offset(0) 0.0 set mom_kin_4th_axis_center_offset(1) 0.0 set mom_kin_4th_axis_center_offset(2) 0.0 set mom_kin_4th_axis_rotation standard set mom_kin_4th_axis_zero_position 0.0
  set mom_kin_5th_axis_plane ZX set mom_kin_5th_axis_center_offset(0) XX set mom_kin_5th_axis_center_offset(1) YY set mom_kin_5th_axis_center_offset(2) ZZ set mom_kin_5th_axis_rotation standard set mom_kin_5th_axis_zero_position 0.0

## Slide 24: Figure 5, Head Table

## Slide 25: Figure 6, Head Table Offsets

## Slide 26: Head Table Kinematics
The following lines define the machine tool as shown in figure 5
  set mom_kin_machine_type 5_axis_head_table
  set mom_kin_4th_axis_plane YZ
  set mom_kin_4th_axis_center_offset(0) 0.0
  set mom_kin_4th_axis_center_offset(1) 0.0
  set mom_kin_4th_axis_center_offset(2) 0.0
  set mom_kin_4th_axis_rotation standard
  set mom_kin_4th_axis_zero_position 0.0
  set mom_kin_pivot_gauge_offset 100.0
  set mom_kin_5th_axis_plane ZX
  set mom_kin_5th_axis_center_offset(0) XX
  set mom_kin_5th_axis_center_offset(1) YY
  set mom_kin_5th_axis_center_offset(2) ZZ
  set mom_kin_5th_axis_rotation standard
  set mom_kin_5th_axis_zero_postion 0.0

## Slide 27: Figure 1, Dual Head

## Slide 28: Figure 3, Dual Table

## Slide 29: Figure 5, Head Table

## Slide 30: Figure 7, Deckel Maho, DMC80U

## Slide 31: Figure 8, Deckel Maho DMC80U Offsets

## Slide 32: DMC80U Kinematics
For machine tools with axis not in principal planes, you must use the NONE value for the axis plane and either direction cosines or angles to specify the axis of rotation of the table.
The following lines define the machine tool as shown in figures 7 and 8.
  set mom_kin_machine_type 5_axis_head_table
  set mom_kin_4th_axis_plane NONE
  set mom_kin_4th_axis_center_offset(0) 0.0
  set mom_kin_4th_axis_center_offset(1) 0.0
  set mom_kin_4th_axis_center_offset(2) 0.0
  set mom_kin_4th_axis_rotation standard
  set mom_kin_4th_axis_zero_position 0.0
Using direction cosines
  set mom_kin_4th_axis_vector(0) 0.0000
  set mom_kin_4th_axis_vector(1) 1.0000
  set mom_kin_4th_axis_vector(2) 1.0000
Using two angles
  set mom_kin_4th_axis_angles(0) 90.0
  set mom_kin_4th_axis_angles(1) 45.0

## Slide 33: DMC80U Kinematics (cont)
The following lines define the machine tool as shown in figures 7 and 8.
The distance from the spindle gauge point to pivot point (the point about which the head rotates) needs to be defined using the kinematics array variable mom_kin_gauge_to_pivot.
  set mom_kin_gauge_to_pivot(0) XX (X-Head Offset)
  set mom_kin_gauge_to_pivot(1) YY (Y-Head Offset)
  set mom_kin_gauge_to_pivot(2) ZZ (Z-Head Offset)
  set mom_kin_5th_axis_plane NONE
  set mom_kin_5th_axis_center_offset(0) 0
  set mom_kin_5th_axis_center_offset(1) 0.0
  set mom_kin_5th_axis_center_offset(2) 0.0
  set mom_kin_5th_axis_rotation standard
  set mom_kin_5th_axis_zero_position 0.0
Using direction cosines :
  set mom_kin_5th_axis_vector(0) 0.0000
  set mom_kin_5th_axis_vector(1) 0.0000
  set mom_kin_5th_axis_vector(2) 1.0000
Using two angles:
  set mom_kin_5th_axis_angles(0) 0.0
  set mom_kin_5th_axis_angles(1) 0.0

## Slide 34: Figure 9, Deckel Maho DMU70V

## Slide 35: Figure 10, Deckel Maho DMU70V Offsets

## Slide 36: DMU70V Kinematics
For machine tools with axis not in principal planes, you must use the NONE value for the axis plane and either direction cosines or angles to specify the axis of rotation of the table.
The following lines define the machine tool as shown in figures 9 and 10.
  set mom_kin_machine_type 5_axis_dual_table
  set mom_kin_4th_axis_plane NONE
  set mom_kin_4th_axis_center_offset(0) 0.0
  set mom_kin_4th_axis_center_offset(1) 0.0
  set mom_kin_4th_axis_center_offset(2) 0.0
  set mom_kin_4th_axis_rotation standard
  set mom_kin_4th_axis_zero_position 0.0
Using direction cosines.
  set mom_kin_4th_axis_vector(0) 0.0000
  set mom_kin_4th_axis_vector(1) -1.0000
  set mom_kin_4th_axis_vector(2) 1.0000
Using two angles
  set mom_kin_4th_axis_angles(0) 270.0
  set mom_kin_4th_axis_angles(1) 45.0

## Slide 37: DMU70V Kinematics (cont)
The following lines define the machine tool as shown in figures 9 and 10.
The distance from the center of the C-axis table to the point about which the 4th axis or independent axis rotates is defined using the kinematics array variable mom_kin_5th_axis_center_offset. Usually, the 4th axis rotation vector and 5th axis rotation vector are coplanar.
  set mom_kin_5th_axis_plane NONE
  set mom_kin_5th_axis_center_offset(0) 1.0
  set mom_kin_5th_axis_center_offset(1) -100.0
  set mom_kin_5th_axis_center_offset(2) -75.0
  set mom_kin_5th_axis_rotation standard
  set mom_kin_5th_axis_zero_position 0.0
Using direction cosines :
  set mom_kin_5th_axis_vector(0) 0.0000
  set mom_kin_5th_axis_vector(1) 0.0000
  set mom_kin_5th_axis_vector(2) 1.0000
Using two angles:-
  set mom_kin_5th_axis_angles(0) 0.0
  set mom_kin_5th_axis_angles(1) 0.0