## Slide 1: Starting UG Post
Stan Suderman

## Slide 2: UG Post Workshop Setup
Type ugmenu and select v16
Enter manufacturing
Open part mypart.prt
Select the operations to postprocess with the operation navigator
Select a post from the list.
Select apply

## Slide 3: Configurations
Directory of .dat files
Default .dat file
All file names are displayed
Select when initializing
Change in Preferences

## Slide 4: What’s in the Configuration File?
Template Set
Documentation Templates
Postprocessors
User defined events
CLS formats
Listing Format
Libraries
Process Assistant (formerly Wizard)

## Slide 5: Sample Configuration File mill_contour.dat
TEMPLATE_OPERATION, ${UGII_CAM_TEMPLATE_SET_DIR}mill_contour.opt
TEMPLATE_DOCUMENTATION, ${UGII_CAM_SHOP_DOC_DIR}shop_doc.dat
TEMPLATE_POST, ${UGII_CAM_POST_DIR}template_post.dat
USER_DEFINED_EVENTS, ${UGII_CAM_USER_DEF_EVENT_DIR}ude.cdl,
${UGII_CAM_USER_DEF_EVENT_DIR}ude.tcl
TEMPLATE_CLSF, ${UGII_CAM_TOOL_PATH_DIR}template_clsf.dat
LISTING_FORMAT, ${UGII_CAM_TOOL_PATH_DIR}clsf.def,
${UGII_CAM_TOOL_PATH_DIR}clsf_listing.tcl
LIBRARY_TOOL, ${UGII_CAM_LIBRARY_TOOL_ASCII_DIR}dbc_tool_ascii.def,
${UGII_CAM_LIBRARY_TOOL_ASCII_DIR}dbc_tool_ascii.tcl
LIBRARY_MACHINE, ${UGII_CAM_LIBRARY_MACHINE_ASCII_DIR}dbc_machine_ascii.def,
${UGII_CAM_LIBRARY_MACHINE_ASCII_DIR}dbc_machine_ascii.tcl
LIBRARY_FEEDS_SPEEDS, ${UGII_CAM_LIBRARY_FEEDS_SPEEDS_ASCII_DIR}feeds_speeds.def,
${UGII_CAM_LIBRARY_FEEDS_SPEEDS_ASCII_DIR}feeds_speeds.tcl
LIBRARY_PART_MATERIAL, ${UGII_CAM_LIBRARY_FEEDS_SPEEDS_ASCII_DIR}part_materials.def,
${UGII_CAM_LIBRARY_FEEDS_SPEEDS_ASCII_DIR}part_materials.tcl
LIBRARY_TOOL_MATERIAL, ${UGII_CAM_LIBRARY_FEEDS_SPEEDS_ASCII_DIR}tool_materials.def,
${UGII_CAM_LIBRARY_FEEDS_SPEEDS_ASCII_DIR}tool_materials.tcl
LIBRARY_CUT_METHOD, ${UGII_CAM_LIBRARY_FEEDS_SPEEDS_ASCII_DIR}cut_methods.def,
${UGII_CAM_LIBRARY_FEEDS_SPEEDS_ASCII_DIR}cut_methods.tcl
WIZARD, ${UGII_CAM_WIZARD_DIR}wizard_mill_contour.tcl

## Slide 6: Mach directory structure
All the resource files are in one place
The custom directory may be used for customized postprocessors, configuration files, shop docs, etc.
Environment variables are used to specify where the system looks for files.

## Slide 7: Format of MOM dat files
Posts, CLSF, ShopDocs
Each line contains 3 fields
Mill 3 axis fast, mill3ax_fast.tcl, mill3ax_fast.def
Mill 3 axis review, mill3ax_review.tcl, mill3ax_fast.def
Fanuc NURBS, fanuc_nurbs.tcl, fanuc_nurbs.def
Mikron NURBS, mikron_nurbs.tcl, mikron_nurbs.def
Roders Poly, roders_poly.tcl, roders_poly.def
Siemens Poly, siemens_poly.tcl, siemens_poly.def
Dialog Name
Event Handler
Definition File

## Slide 8: Postprocessors
TEMPLATE_POST,
${UGII_CAM_POST_DIR}template_post.dat
MILL 3_AXIS,
${UGII_CAM_POST_DIR}mill3ax.tcl,${UGII_CAM_POST_DIR}mill3ax.def
MILL 4_AXIS,
${UGII_CAM_POST_DIR}m4bh.tcl,${UGII_CAM_POST_DIR}m4bh.def
MILL 5_AXIS,
${UGII_CAM_POST_DIR}m5abtt.tcl,${UGII_CAM_POST_DIR}m5abtt.def
...
List of posts
MOM application
Replacing the generic machine with a library machine changes the list

## Slide 9: Where are things defined?
Configuration
file
TEMPLATE_POST,
${UGII_CAM_POST_DIR}template_post.dat
ugii_env
file
UGII_CAM_POST_DIR=${UGII_CAM_RESOURCE_DIR}
postprocessor/

## Slide 10: How To Customize Your Posts
Edit the .ugii_env file as follows:
  UGII_CAM_POST_DIR=${UGII_CAM_CUSTOM_DIR}postprocessor/
Copy the template_post.dat file and any of the generic posts you want to keep to your new post directory.
Edit your new template_post.dat file to reflect the posts you want to use.

## Slide 11: Exercise 1
Use Help -> Log file to see where UG in installed, and verify what resource directory you are using.
Copy the resource directory structure from mach to your home directory
Give yourself write access to your resource files.
Tell CAM to use your resource files (one way to do it)
Copy the UG environment file from the install to your home
  Change the line that defines the resource directory
  On Unix, the file is .ugii_env
    UGII_CAM_RESOURCE_DIR=${HOME}/resource/
  On NT, the file is ugii_env.dat
    UGII_CAM_RESOURCE_DIR=d:\users\resource\
  Don’t forget the trailing / or \
Restart Unigraphics
Use Help -> Log file to verify that your resource directory is being used.

## Slide 12: Exercise 2
Create a postprocessor
In your resource/postprocessor directory copy mill3ax.def to mypost.def and mill3ax.tcl to mypost.tcl
Edit template_post.dat and add your post.
Verify that UG knows about your post by postprocessing and see your post on the list.

## Slide 13: Exercise 3
Turn on the review tool.
Remove the # from the following two lines in your tcl file.
  # source [MOM_ask_env_var UGII_CAM_DEBUG_DIR]mom_review.tcl
  # MOM_set_debug_mode ON

## Slide 14: Solution 1
cd
cp –R /cyp/netug04/osf/ugs16022/mach/resource .
chmod –r 777 resource