## Slide 1: Post Processing with UG POST
Stan Suderman

## Slide 2: UG Post Topics
Background
UG Post (MOM) Architecture
Customizing Your System
Event Generator
Definition File
5 Axis Kinematics
Event Handler
Tcl
User Defined Events
Installing WISH
Debugging Tools
Inheritance
Post Builder
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3: V15 Postprocessing Situation
GPM
  6000 Users
  Good for standard machines
  Poor for customization requirement
  Loyal user base
  Low Priced vs Competition

## Slide 4: Drivers for UGPost
GPM Limitations
  Limited Coverage
  Difficult to add new technology
Integrated NC Post Processing
Compatible with New CAM Architecture
  Access to operation data and internal tool path
  Access to machine tool information
  Access to tool information
  Access UG Part info for documentation
Shift to Direct Post Processing Paradigm
  CLSF no longer required

## Slide 5: Positioning
UG Post is our mainstream post processing solution
New functions will only be developed in UGPost
GPM is going into maintenance mode
No direct data conversion between MDF and UGPost

## Slide 6: Benefits of UGPost
Reduces processing time by going from tool path directly to post processed output
Capable of addressing simple to extremely complex machines
Reduces Post development time
Platform for new technology

## Slide 7: What is the Manufacturing Output Manager (MOM) ?
Architecture/Mechanism to access UG data and generate formatted output
Many UG applications will be based on MOM
  UGPost
  UGShop Docs
  UG Library Mechanism

## Slide 8: What is UGPost ?
Application based on the MOM Architecture
Full capability postprocessor
Innovative approach
Highly extensible
Components
  UGPost Execute
  UGPost Builder

## Slide 9: Typical structure and semantics of a NC program
Sequence of blocks which represents an instruction to the controller.
Each block is a sequence of words separated by a separator and terminated by an end of line.
Each word is a combination of an address and a value.
An address specifies where to store the value.
The value is either a number or a string.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Example:
(Created By: murgolo)
(TASK: /cam/v130/post_demo/demo.prt)
%
(Creation Date: Thu May 29 17:17:35 1997)
G54 H0 D0 T0
T02
(-----------------------------------------------)
(Start path: PROFILE with tool: MILL-.5)
(-----------------------------------------------)
N02 G28 X0.0000 Y0.0000 G49 Z0.0000 M04
N12 T02
N22 G01 X-4.1970 Y3.4533 F50.0
N32 G00 G43 Z2.1 M03
N42 Z1.6 F5.00
N52 Z1.5 F2.0
N62 X-3.847
N72 X3.8470 F3.0
N82 G02 X4.3470 Y2.9533 I0.5 J0.0 K0.0
N92 G01 Y-2.0763
N102 G02 X3.8470 Y-2.5763 I0.0 J-0.5
N112 G01 X-3.8470
N122 Z2.2 F5000.0
N132 X-4.0762 Y3.5534
N462 G03 X-4.047 Y-2.4263 I-0.2 J0.15 F1000.0
N472 (End Of Path PROFILE)
N482 M30
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: UG Post Architecture
UG Data Storage
UG Post
Event
Generator
Event Handler
Definition File
Output File
Event Name
variable
variable
variable
User Defined

## Slide 12: UG Post Architecture
UG
UG Post
Event
Generator
Linear Move
Format
G01 X# Y# Z#
G01 X1. Y2. Z3.
(1,2,3)
GOTO/1,2,3

## Slide 13: UG Post Architecture
UG Data Storage
Linear Move
x = 100
y = 50
z = 75
UG Post
Event
Generator
proc Linear_Move {
MOM_do_template Linear
}
Format Socket %0.3f
Address X
{Format Socket Min 0 Max 550}
BLOCK_TEMPLATE Linear
{ G01 X[$x] Y[$y] Z[$z] }
G01 X100. Y50. Z75.
Linear_Move
x = 100
y = 50
z = 75

## Slide 14: UG reads a command in the path entity and generates a corresponding event
UG Data Storage
Linear Move
x = 100
y = 50
z = 75
UG Post
Event
Generator
proc Linear_Move {
MOM_do_template Linear
}
Format Socket %0.3f
Address X
{Format Socket Min 0 Max 550}
BLOCK_TEMPLATE Linear
{ G01 X[$x] Y[$y] Z[$z] }
G01 X100. Y50. Z75.
Linear_Move
x = 100
y = 50
z = 75
1
1

## Slide 15: The event generator sends the event to UG Post
UG Data Storage
Linear Move
x = 100
y = 50
z = 75
UG Post
Event
Generator
proc Linear_Move {
MOM_do_template Linear
}
Format Socket %0.3f
Address X
{Format Socket Min 0 Max 550}
BLOCK_TEMPLATE Linear
{ G01 X[$x] Y[$y] Z[$z] }
G01 X100. Y50. Z75.
Linear_Move
x = 100
y = 50
z = 75
2
2

## Slide 16: UG Post passes the event on to the Event Handler, who decides what to do.
UG Data Storage
Linear Move
x = 100
y = 50
z = 75
UG Post
Event
Generator
proc Linear_Move {
MOM_do_template Linear
}
Format Socket %0.3f
Address X
{Format Socket Min 0 Max 550}
BLOCK_TEMPLATE Linear
{ G01 X[$x] Y[$y] Z[$z] }
G01 X100. Y50. Z75.
Linear_Move
x = 100
y = 50
z = 75
3
3

## Slide 17: UG Post reads the block template ‘Linear’ and uses it to format an output block
UG Data Storage
Linear Move
x = 100
y = 50
z = 75
UG Post
Event
Generator
proc Linear_Move {
MOM_do_template Linear
}
Format Socket %0.3f
Address X
{Format Socket Min 0 Max 550}
BLOCK_TEMPLATE Linear
{ G01 X[$x] Y[$y] Z[$z] }
G01 X100. Y50. Z75.
Linear_Move
x = 100
y = 50
z = 75
4
4

## Slide 18: UG Post outputs the block to the output file
UG Data Storage
Linear Move
x = 100
y = 50
z = 75
UG Post
Event
Generator
proc Linear_Move {
MOM_do_template Linear
}
Format Socket %0.3f
Address X
{Format Socket Min 0 Max 550}
BLOCK_TEMPLATE Linear
{ G01 X[$x] Y[$y] Z[$z] }
G01 X100. Y50. Z75.
Linear_Move
x = 100
y = 50
z = 75
5
5

## Slide 19: Basic UG Post Concepts
Events
Unigraphics Event Generator
Event Handler
Definition File
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20: Events
An event is data extracted from a UG part file.
Each event is associated with a set of variables defining that event.
For each event recognized by the event generator, its corresponding Tcl procedure is executed.
For example, the x,y,z variables of a linear move in UG defines the end position of a linear move event.
These variables will be passed to the event handlers as global variables. In this way the variables are available to all procedures.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: Unigraphics Event Generator
The event generator extracts the tool path data from UG and passes it to the UG Post as events and variables.
The event generator performs many of the traditional post processing functions for the user. These include:
  Parsing post commands into global variables
  Applying kinematic to the goto points.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22: Event Generator Example
Tool Path Post Command
  SPINDL/RPM,100,CLW
Event generator parses the command and creates an event.
  Event
    MOM_spindle_rpm
  Global Data
    mom_spindle_speed = 100
    mom_spindle_direction=3
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: Examples of some events and variables loaded by the Event Generator
MOM_start_of_program
  When Triggered: The first event.
  Variables Loaded:
    mom_date
    mom_log_name
MOM_start_of_path
  When Triggered: The first event of each operation's tool path.
  Variables Loaded:
    mom_path_name
    mom_tool_name
    mom_part_name
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: Examples of Some events and variables loaded by the Event Generator
MOM_tool_change (if necessary)
  When Triggered: After the start of path event, if tool is different from the previous tool.
  Variables Loaded:
    mom_tool_number
    mom_tool_adjust_register
MOM_initial_move
  When Triggered: The first move after a tool change.
  Variables Loaded:
    mom_pos(0)
    mom_pos(1)
    mom_pos(2)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25: Definition File
The definition file describes the static characteristics of the blocks and the available addresses for a specific machine. It contains the following components:
  The block structure for each type of instruction (e.g., linear move, circular move, tool change).
  The available addresses.
  The word separator and line terminator.
  The format definitions.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 26: Block Template Example
BLOCK_TEMPLATE Linear {
    G[01]
    X[$mom_pos(0)]
    Y[$mom_pos(1)]
    Z[$mom_pos(2)]
    F[$mom_feed_rate]
    }
Notes: <number>
<footer>
<header>
<date/time>

## Slide 27: Address Example:
  ADDRESS F {
  FORMAT Feed
  MAX 12000.00
  MIN 0
  FORCE off
  }
Notes: <number>
<footer>
<header>
<date/time>

## Slide 28: Format
format definition: &abcdef
  a = + or _ “+” means output the plus sign, “_” means suppress the plus sign.
  b = 0 or _ “0” means output leading zeros, “_” means suppress leading zeros.
  c = {0,1,…,9} Maximum number of digits to left of decimal.
  d = . or _ “.” means output the decimal, “_” means don’t output the decimal
  e = {0,1,…,9} Maximum number of digits to right of decimal.
  f = 0 or _ , “0” means output leading zeros, “_” means suppress leading zeros.
C language format: Any valid C printf format.
Example:
    FORMAT Feed “&__4.2_”
Notes: <number>
<footer>
<header>
<date/time>

## Slide 29: Word Separator
The word separator defines the string that will be placed between words in a block.
    WORD_SEPARATOR <string>
string: Any string literal.
Example:
    WORD_SEPARATOR " "
Notes: <number>
<footer>
<header>
<date/time>

## Slide 30: End Of Line
The end of line defines the string that will be placed at the end of a block.
    END_OF_LINE <string>
string: Any string literal.
Example:
    END_OF_LINE "\012"
Notes: <number>
<footer>
<header>
<date/time>

## Slide 31: Event Handler features
Tcl
Tcl extensions
UG Post Base
Multi-axis Kinematics

## Slide 32: Event Handler
The event handler is a Tcl procedure that determines how a tool path event will be processed.
Each event handler will determine if output is to be generated and, if it is, which blocks will be output.
UG extends the Tcl language to allow users to easily construct output blocks based on the definition file. These extensions will be available to call from within an event handler.
The event handler can also process the variables loaded by the event generator before outputting a block.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 33: Introduction to Tcl
The language of the event handler for UG Post.
Tcl is pronounced "tickle" or "tee see ell".
An interpreted language.
Developed by John K. Ousterhout while at UC Berkeley.
Currently supported by Scriptix Corp. (web site www.scriptics.com)
Public domain and available on all currently supported UG platforms.
The official UG language for user-supplied rules.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 34: Tcl Example:
proc MOM_linear_move {} {
  global first_motion
  if {$first_motion != 1} {
  MOM_force_once X Y Z
  set first_motion 1
  }
  MOM_do_template linear
  }
Notes: <number>
<footer>
<header>
<date/time>

## Slide 35: Basic Tcl syntax:
Tcl code is contained in a Tcl script.
The script can contain code inside of procs and code outside of procs.
The code outside of a proc is executed when the interpreter reads the script.
The code inside of a proc is only executed when the proc is called.
Allows for local and global variables.
Has numeric, string, logical and relational operations.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 36: Basic Tcl syntax (con’t):
Very strong string processing.
Has control structures if, while, for, foreach, break, continue, switch, eval, expr, source.
Highly extensible, i.e., can add new commands to the interpreter very easily.
Has facilities for error handling, file I/O, process spawning and limited debugging.
Allows for easy building of GUI interfaces by using Tk.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 37: Tcl Programming Example:
proc fact x {
if { $x <= 1 } { return 1 }
[expr $x * [fact [expr $x - 1]]]
}
# Main
if { $argc != 2 } {
  puts "Usage: \
  $argv0 <inputfile> \
  <output file>"
  exit 1
}
set infile [open [lindex argv 0] r]
set outfile [open [lindex \
argv 1] w]
while { [gets $infile \
number] >= 0 } {
  set value [fact $number]
  puts $outfile $value
}
close $infile
close $outfile
# Now remove input file
exec rm [lindex argv 1]
Notes: <number>
<footer>
<header>
<date/time>

## Slide 38: UG Post Extensions to Tcl
The components of the definition file can be used as input to the Tcl extension commands.
The primary purpose of these commands is to construct NC output blocks.
All Tcl extension commands are prefixed with the string MOM_.
UG Post also allows users to add their own commands to Tcl.
The following are a few of the main UG Post Tcl commands along with their primary inputs:
Notes: <number>
<footer>
<header>
<date/time>

## Slide 39: MOM_do_template
Evaluate and output a block based on a block template that is defined in the definition file.
Input
  template name
Example
  MOM_do_template linear
Notes: <number>
<footer>
<header>
<date/time>

## Slide 40: MOM_output_literal
Output a list of literals and variables as single line.
Input
  string
Example:
  MOM_output_literal "Start of path $mom_path_name"
Notes: <number>
<footer>
<header>
<date/time>

## Slide 41: MOM_suppress_address
The next time a block template is evaluated that contains a reference to any of the input address names, the word that contains the address will not be output regardless of its modality attribute.
Input
  modality (once, always, never)
  address names
Example:
  MOM_suppress_address once N X Y
Notes: <number>
<footer>
<header>
<date/time>

## Slide 42: Where is wish and How do I get it?
Outline the steps to retrieve and load wish for:
  Windows NT
  UNIX

## Slide 43: User Defined Events
Allows the customization of the Machine Control Dialog with additional or special Post commands
Allows users to create MOM variables
Extracts information from the UG part file for use in the post processor

## Slide 44: UG Post Base Files
Library of standard utilities
  Feedrate modes (IPM, IPR, FRN)
  Spindle modes (SFM, RPM)
  INSERT, PPRINT
Handles listing output
Error handling

## Slide 45: New 5 Axis Kinematics
New procedures to use for correctly determining multi-axis positioning
Additional libraries available for non-orthogonal machine axis (Deckel-Maho)

## Slide 46: Debugging Tools
There are three events that were added to support debugging tools.
  MOM_before_each_event - This event is automatically triggered before each event created by the event generator. The event name will be loaded into the variable mom_debug_event_name.
  MOM_before_each_add_var - This event is automatically triggered just before a variable is loaded. The variable name and its value will loaded into mom_debug_assign_var in the format of <var_name> = <value>.
  MOM_before_load_address - This event is automatically triggered before an address is loaded with a new value.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 47: Mom_debug.tcl
UG provides debugging tools that uses these three events. One of the tools tool is a tcl file named mom_debug.tcl. The user includes this file into their event handler to activate debugging for that event handler.
  It stops at each event and lists the variables that were loaded for that event.
  It creates a trace file of all the events and their associated variables.
For performance reasons, we only automatically call the debug events if they exist in the currently loaded event handler.

## Slide 48: Mom_review.tcl
UG also provides a debugging tool that displays debugging information in three window panels.
  One panel is a list of events.
  The middle panel is all the data for the event.
  The other panel lists the NC code.

## Slide 49: Inheritance of definition files and event handler files
A definition file can include other definition files using the INCLUDE <file name> command inside a definition file.
An Event Handler file can include other event handler files using the Tcl command "source <file name>"
By using the INCLUDE and the source statements you can produce similar post processors by inheriting the definitions and event handlers of one or more other post processors and then overriding just those in the new definition file.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 50: Alternate Inputs to UGPost
UG Post
Event
Generator
UG Part
Event
Generator
Event
Generator
UG CLSF
Other Vendor Formats
Event
Handler
Definition
File
Output File

## Slide 51: UGPost Products
UGPost Execute
  Used to postprocess from a UG Part file
  Analogous to GPM
UGPost Builder
  Used to create or edit a post
  Analogous to MDFG

## Slide 52: UGPost Builder
Scalable
  Mill, Lathe, Advanced
User Interface
  State of the art tool
  Graphical
  Provide feedback on kinematics
Capabilities
  Machine tool kinematics
  Block templates
  Address definitions
  Formats
Notes: <number>
<footer>
<header>
<date/time>

## Slide 53: V16 UG Postprocessing
UG Post Builder
  Users will be able to create postprocessors with an interactive tool.
UG Custom Posts
  UG will develop custom postprocessors based on customer requirements.
UG Post created by users based on the tools provided.

## Slide 54: V17 Target Projects
UGPost Builder (phase II)
  Lathe
  Wire EDM
Mill Turns
Merging Lathes
Alternate Inputs

## Slide 55: Transition from MDFG/GPM
License Conversion (Grand fathering)
GPM on critical maintenance
At least a two year overlap